## Slide 1: What is Spice?
Spice is the short form of:
  Simulated
  Program with
  Integrated
  Circuit
  Emphasis

## Slide 2: PSPICE Programming
Why PSPICE Programming
Steps of Programming
Statements
Data Statements
Control Statements
Example Circuits

## Slide 3: Why PSPICE Programming
Don’t have to draw the circuit
More control over the parts
More control over the analysis
Don’t have to search for parts
Some SPICE softwares (HSPICE etc.) don’t have GUI at all
Quick and efficient

## Slide 4: Steps of Programming
Draw the circuit and label the nodes
Create netlist (*.cir) file
Add in control statements
Add in title, comment & end statements
Run PSPICE
Evaluate the results of the output

## Slide 5: Statements
Different statements:
  Not case sensitive
  Title: first line of code (always)
  .END <CR>: last line of code (always)
  Comment: line denoted by *
  Comment within a statement is preceded by a semicolon (;)
  + means continuation of a sentence
  Data: resistor, capacitor, etc.
  Control: analysis and output

## Slide 6: Data Statements
Resistor
  R<name> <node1> <node2> <value>
  Example: R1 1 2 100
Capacitor
  C<name> <node1> <node2> <value>
  Example: Cs 13 0 1u
Inductor
  L<name> <node1> <node2> <value>
  Example: LR 5 4 1m

## Slide 7: Data Statements
Independent Voltage Source
  V<name> <+ node> <- node> [[DC] <value>] [AC <magnitude> [phase]] [transient + specification]
3 types of sources:
  DC: Vin 1 0 5
  AC: Va 4 0 AC 25
  Transient

## Slide 8: Data Statements
Transient Source
  Vname <n+> <n-> SIN(Vo Va freq td phase)
  Vname <n+> <n-> PULSE(V1 V2 Td Tr Tf Pw Period)
  Vname <n+> <n-> PWL(t1,v1,t2,v2,…,tn,vn)

## Slide 9: Data Statements
Independent Current Source
  I<name> <+ node> <- node> [ [DC] <value> ] [AC <magnitude> [phase]] [transient + specification]
Same as Independent Voltage Source

## Slide 10: Data Statements
MOSFET
  M<name> <drain node> <gate node> <source node> <substrate node> <model name> [L=<value>] [W = <value>]
  .MODEL <model name> <NMOS or PMOS> [model parameters]
Example:
  M1 1 2 3 3 NTYPE W=10U L=50U
  .MODEL NTYPE NMOS (VTO=-3 KP=1E-5)

## Slide 11: Data Statements
MOSFET Parameters
Parameter | Description | Default value
VTO | Threshold voltage | 0
KP | Conductance parameter | 0.02 mA/V2
CBD | Drain-to-substrate capacitance | 0
CBS | Source-to-substrate capacitance | 0
TOX | Oxide-layer thickness | 10-7 m

## Slide 12: Data Statements
Sub Circuit
.SUBCKT Example_1 5 12 18 Iw 10 12 10A Ra 5 12 5.0 Rb 5 13 4.0 Rc 12 13 2.0 Rd 5 18 8.0 Re 13 18 3.0 Rf 10 13 1.0 Rg 10 18 6.0 .ENDS

## Slide 13: Data Statements
.INLUDE Exampl_1.CIR
Vs 1 0 50
Iq 5 0 15
Ra 1 2 1
Rb 3 4 3
Rc 7 0 25
Rd 6 0 45
X1 2 7 3 Example_1
X2 4 6 5 Example_1
.END

## Slide 14: Data Statements
Suffixes
f | femto | 10-15
p | pico | 10-12
n | nano | 10-9
u | micro | 10-6
m | milli | 10-3
k | kilo | 103
meg | mega | 106
g | giga | 109
t | tera | 1012

## Slide 15: Control Statements
Analysis Types
  DC Analysis: .DC
  AC Analysis: .AC
  Transient Analysis: .TRAN
Output Format
  Text Output: .PRINT, .PLOT
  Graph Output: .PROBE

## Slide 16: DC Analysis
Format
  .DC <source> <vstart> <vstop> <vincr> [src2 start2 stop2 incr2]
Example:
  .DC Vin 0.25 5.0 0.25
  .DC Vds 0 10 0.5 Vgs 0 5 1

## Slide 17: DC Analysis
PLOT I-V Characteristics of NMOS
  VTO = +1V
  KP = 30u
MOSFET I-V Characteristics
M1 1 2 0 0 NTYPE
.MODEL NTYPE NMOS(VTO=1 KP=30u)
Vgs 2 0 5
Vds 1 0 5
.PROBE
.PRINT DC I(Vds)
.DC Vds 0 5 .5 Vgs 0 5 1
.END
ID
G
D
S

## Slide 21: AC Analysis
Format
  .AC <sweep type> <points value> <start frequency> <end frequency>
  <sweep type> is either LIN, OCT, or DEC
Example
  .AC LIN 1 60Hz 600Hz
  .AC LIN 11 100 200
  .AC DEC 20 1Hz 10kHz

## Slide 22: AC Analysis
60 Hz AC Circuit
Vs 1 0 AC 120V 0
Rg 1 2 0.5
Lg 2 3 3.183mH
Rm 3 4 16.0
Lm 4 0 31.83mH
Cx 3 0 132.8uF
.AC LIN 1 60 60
.PRINT AC VM(3) VP(3) IM(Rm) IP(Rm) IM(Cx) IP(Cx)
.END

## Slide 25: AC Analysis
Second-Order High-Pass Filter
Vin 1 0 AC 10V
Rf 1 2 4.0
Cf 2 3 2.0uF
Lf 3 0 127uH
.AC DEC 20 100Hz 1MEG
.PROBE
.END

## Slide 28: Transient Analysis
Format
  .TRAN <print step> <final time> [no-print value]
Example
  .TRAN 1n 1000n
  .TRAN 1n 1000n 500n

## Slide 29: Transient Analysis
CMOS Inverter
Vin 1 0 pulse(0 5 0 1p 1p 5n 10n)
Vdd 3 0 5
M2 2 1 3 3 PTYPE W=5u L=2.5u
M1 2 1 0 0 NTYPE W=5u L=5u
.MODEL PTYPE PMOS(KP=15u VTO=-1)
.MODEL NTYPE NMOS(KP=30u VTO=1)
.PROBE
.TRAN 1n 20n
.END
0
2
3
1